## Slide 1
AEROSOL TRANSFER EFFICIENCY OF ETHYL MALTOL IN COMMERCIAL ENDS
Manoj Misra, Lise Fraissinet and Ed Carmines
Chemular Inc, Hudson MI, USA
Poster # 89
ABSTRACT
STUDY DESIGN AND METHODS
Method validation and analytical testing was conducted at Spark Lab,, Gdynia, Poland.
RESULTS
CONCLUSIONS
Ethyl maltol has a sweet fruit-like odor and is a common flavor ingredient used in ENDS e-liquids used at high concentration.
The methods for the determination of ethyl maltol in e-liquid matrix and its transfer in aerosol was established.
The non-intense vaping regiment utilized was non-intense (CORESTA CRM81) and intense vaping regiment utilized.
The aerosol transfer efficiency of ethyl maltol from e-liquid for tested Pod-ENDS was high (non-intense vaping, ~81-94% and intense vaping, ~76-92%).
The results indicate high ethyl maltol aerosol transfer efficiency from e-liquids in various commercially available ENDS and may impact the ENDS ELCR calculations.
Ethyl maltol has a sweet fruit-like odor and is a common flavor ingredient in ENDS e-liquids. The transfer of the ethyl maltol in aerosol is dependent on the device characteristics. The conservative approach to estimate potential exposure of the flavor chemicals to consumer from the aerosol is to assume 100% transfer from the e-liquid. The frequent and high use of ethyl maltol in e-liquid has the potential to drive a concern about the excess lifetime cancer risk (ELCR).
Therefore, the level of ethyl maltol in e-liquids and its transfer efficiency to aerosol under non-intensive and intensive vaping regime was determined in commercially available tobacco flavored pod-based ENDS. The non-intense vaping regiment utilized was CORESTA CRM81 (puff volume 55 ml; puff duration 3sec; puff interval 30sec.) The intense vaping regiment utilized was, puff volume 110 ml; puff duration 5sec; puff interval 30sec. The methods for the determination of ethyl maltol in e-liquid matrix and its transfer in aerosol was established. Under non-intense vaping conditions, ethyl maltol in commercially pod-based ENDS products transferred at a rate of 85 to 93%. As a comparison, the ethyl maltol in NJOY Ace Classic Tobacco transferred at a rate of 81%. Under intense vaping conditions, ethyl maltol in commercially pod-based ENDS products transferred at a rate of 78 to 91%. As a comparison, the ethyl maltol in NJOY Ace Classic Tobacco transferred at a rate of 76%. The results indicate high ethyl maltol aerosol transfer efficiency from e-liquids in various commercially available ENDS and may impact the ENDS ELCR calculations.
E-LIQUID METHOD VALIDATION
78th TSRC Conference 2025, Knoxville, TN, USA
Compound
VALIDATION SAMPLES
AEROSOL METHOD VALIDATION
Compound | CAS Number | Description | Purity
Ethyl Maltol | 4940-11-8 | White crystalline powder | 99.00%
Ethyl Maltol
(IUPAC name: 2-Ethyl-3-hydroxy-4H-pyran-4-one
COMMERCIAL POD ENDS PRODUCTS ETHYL MALTOL ANALYSIS
ETHYL MALTOL LEVEL IN PRODUCT E-LIQUIDS
ETHYL MALTOL LEVEL IN PRODUCT AEROSOL
E-Liquid Sample: Simulated 5% nicotine in VG/PG (vegetable glycerin:propylene glycol) base 1:1, v/v.
Aerosol Sample: Sample generated by aerosolization of the validation E-liquid sample
AEROSOL GENERATION
Aerosol generation apparatus compliant with ISO 20768:2018.
Coil resistance: 1.5 Ω
Battery voltage: 3.7 V (stable mode) Atomizer capacity: 1.8 ml
Atomiser: Volimizer Volish V4 Pro
PARAMETER | Non-Intense Vaping | Intense Vaping
Number of puffs: | 30 puffs | 
Number of puffs discarded: | first 5 puffs | 
Number of puffs collected for testing: | 25 puffs (6-30) | 
Puff duration: | 3 sec | 5 sec
Puff interval | 30 sec. | 30 sec.
Puff volume (average) | 55 ml | 110 ml
Air flow: | 1.1 L/min | 1.3 L/min
Atomizer: | Product specific | 
Volume in bubbler: | 25 ml of methanol | 
Vaping regime: | square wave | 
LOQ | 0.5003 mg/gram
LOD | 0.2502 mg/gram
ANALYSIS AND METHODANALYTICAL LOD AND LOQ FOR ETHYL MALTOL
Variable | Acceptance Criteria | Results of Ethyl maltol in E-liquid
System suitability | RSD peak areas ≤ 5.0 % r≥0.995 REC 95.0-105.0% S/N for Cal.sol.1 ≥ 10 | RSD% = 4.7% r=0.9999 REC% = 101.4 S/N LOQ = 222
Specificity | Resolution of ethyl maltol peaks with any other peak must be ≥ 1 | Criterion met
Detection and Quantification limits | LOQ S/N ≥10 LOD S/N ≥3 | S/N LOQ = 263 S/N LOD = 19
Linearity | r ≥ 0.995 RSD ≤ 10% | r=0.9997 RSD(u)% = 9.2
Range |  | 0.4996 – 50.1000 mg/g
Method repeatability | RSD ≤ 5.0 % TEP ≤ 0.05 | RSD% = 2.1 TEP = 0.005
Intermediate precision | RSD6 ≤ 5.0 % RSD12 ≤ 7.5 % Diff%< 10 % TEP ≤ 0.05 | RSD%(n=6) = 3.3 RSD%(n=12) = 3.11 Diff% = 3.12 TEP = 0.012
Accuracy | LOQ level | 
 | RSD ≤ 5.0% | RSD% = 0.91
Variable | Recovery 95.0% - 105.0% TEP ≤ 0.05 | REC% = 97.6 TEP = 0.0003
 | Level 2 | 
 | RSD ≤ 5.0% REC 95.0% - 105.0% TEP ≤ 0.05 | RSD% = 0.41 REC% = 99.9 TEP = 0.0097
 | Level 3 | 
 | RSD ≤ 5.0% REC 95.0% - 105.0% TEP ≤ 0.05 | RSD% = 3.16 REC% = 99.1 TEP = 0.0402
Stability | Diff(A) ≤ 5% | Diff(A)20h = 0.35
Robustness | RSD ≤ 5.0% REC 95.0% - 105.0% TEP ≤ 0.05 | RSD 0.49 to 4.4 REC% 98.7 to 107.5 TEP 0.00003 to 0.00004
VALIDATION
PRODUCT TESTED
Analytical Instrument: Gas chromatograph with MS detector
Test Products | E-liquid | Aerosol
Pod ENDS Product 1: Fruit 50mg/mL | X | X
Pod ENDS Product 2: Menthol 50mg/mL | X | X
Pod ENDS Product 3: Tobacco 50mg/mL | X | X
Pod ENDS Product 4: Tobacco 50mg/mL | X | X
Pod ENDS Product 5: Tobacco 50mg/mL | X | X
Pod ENDS Product 6: Tobacco 58mg/mL | X | X
AEROSOL TRANSFER EFFICIENCY OF ETHYL MALTOL FROM PORDUCTS
Test Products | Ethyl Maltol in E-Liquid (mg/gram e-liquid) | 
 | Average | S.D.
Pod ENDS Product 1: Fruit 50mg/mL | 3.3055 | 0.2191
Pod ENDS Product 2: Menthol 50mg/mL | 0.6844 | 0.0359
Pod ENDS Product 3: Tobacco 50mg/mL | 14.4093 | 0.2741
Pod ENDS Product 4: Tobacco 50mg/mL | 13.0481 | 0.2207
Pod ENDS Product 5: Tobacco 50mg/mL | 3.4561 | 0.0893
Pod ENDS Product 6: Tobacco 58mg/mL | 10.5982 | 0.2505
Test Products | Transfer of ethyl maltol in aerosol (mg/gram of E-liquid) |  |  | 
 | Non-Intense vaping |  | Intense vaping | 
 | Average | S.D. | Average | S.D.
Pod ENDS Product 1: Fruit 50mg/mL | 3.0911 | 0.0711 | 3.0294 | 0.0549
Pod ENDS Product 2: Menthol 50mg/mL | 0.582 | 0.0318 | 0.5351 | 0.0058
Pod ENDS Product 3: Tobacco 50mg/mL | 12.692 | 0.275 | 12.1984 | 0.0982
Pod ENDS Product 4: Tobacco 50mg/mL | 11.3009 | 0.2056 | 10.9342 | 0.2476
Pod ENDS Product 5: Tobacco 50mg/mL | 2.949 | 0.0579 | 2.7392 | 0.0595
Pod ENDS Product 6: Tobacco 58mg/mL | 8.62 | 0.2239 | 8.1007 | 0.2031
Test Products | % Ethyl Maltol Transfer Efficiency in Aerosol | 
 | Non-Intense Vaping | Intense Vaping
Pod ENDS Product 1: Fruit 50mg/mL | 93.51 | 91.65
Pod ENDS Product 2: Menthol 50mg/mL | 85.04 | 78.19
Pod ENDS Product 3: Tobacco 50mg/mL | 88.09 | 84.66
Pod ENDS Product 4: Tobacco 50mg/mL | 86.61 | 83.80
Pod ENDS Product 5: Tobacco 50mg/mL | 85.33 | 79.26
Pod ENDS Product 6: Tobacco 58mg/mL | 81.33 | 76.43
Variable | Acceptance criteria | Results of Ethyl maltol in Aerosol
System suitability | RSD ≤5.0 % r≥0.995 REC 95.0-105.0% S/N ≥ 10 | RSD% = 4.7% r=0.9999 REC% = 101.4 S/N LOQ = 222
Specificity | Resolution must be ≥ 1 in standard solution and in test solution spiked (LOQ level) | Criterion met
Detection and Quantification limits | LOQ S/N ≥10; LOD S/N ≥3 | S/N LOQ = 263 S/N LOD = 19
Linearity | r ≥ 0.995 RSD (u) ≤10% | r=0.9997 RSD(u)% = 9.2
Range |  | 6.2450 – 625.5000 µg/puff
Method repeatability | RSD ≤ 10.0 % | RSD% = 2.7
Intermediate precision | RSD6 ≤ 10.0 % RSD12 ≤ 15.0 % Diff < 15 % | RSD%(n=6) = 4.0 RSD%(n=12) = 3.2 Diff% = 0.17
Accuracy | LOQ level | 
 | RSD ≤ 5.0% Recovery 95.0% - 105.0% TEP ≤ 0.05 | RSD% = 0.91 REC% = 97.6 TEP = 0.0003
 | Level 2 | 
 | RSD ≤ 5.0% Recovery 95.0% - 105.0% TEP ≤ 0.05 | RSD% = 0.41 REC% = 99.9 TEP = 0.0097
 | Level 3 | 
 | RSD ≤ 5.0% Recovery 95.0% - 105.0% TEP ≤ 0.05 | RSD% = 3.16 REC% = 99.1 TEP = 0.0402
Stability | Diff(A) ≤ 5% | Diff(A)20h = 2.03
Robustness | RSD ≤ 5.0% REC 95.0% - 105.0% TEP ≤ 0.05 | RSD 0.49 to 4.4 REC% 98.7 to 107.5 TEP 0.00003 to 0.00004